## Slide 1: Advanced Topics in Networking: Special Topics in Internet of Things
Ambuj Varshney
ambujv@nus.edu.sg, http://ambuj.se
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.

## Slide 2
Lecture 6
Processing, IoT Platforms
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 3: Administration
List of paper allocation on the course website. Some students still missing!
  This your final chance or you will be randomly allocated paper!
Think about projects that you want to do in the course:
  Focus on a good hypothesis/ problem statement
  Execution: supporting evidence to go or against the hypothesis
  Do not expect significant engineering effort
Course webpage: http://https://weiserlab.github.io/ambuj/cs6204
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 4: Administration
Akshay - 19th of October, 2pm SGT, Zoom
Nirupam – 12th of 26th October, would 10:30 am work?, Zoom
Mobashir – In-Person
Invited lectures are mandatory to attend!
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 5: Course projects examples – Confluence of wireless and machine learning
Can we leverage machine learning frameworks and enhance wireless links?
Reliability? Channel assignment? Concurrency? ….
What exists in the literature ? Recent works?
What experiments would you want to perform?
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 6: Course projects examples – Low capability camera with Stable Diffusion Img2Img
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 7: Course projects examples – Low capability camera with Stable Diffusion Img2Img
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 8: Course projects examples – Open AI Whisper and Embedded microphones
Bring high accuracy speech recognition to embedded device?
Too power consume to perform locally
Record audio, transmit to computer (Open AI Whisper), send back translated audio to embedded device;
Latency considerations? Other Optimizations etc?
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 9: Course projects examples – TinyML and Sensors
Machine learning techniques with sensor data
Tensorflow Lite on Arduino could be used as a platform
Machine learning sensors (paper to be discussed)
Reduce noise? Improve accuracy? Sensor fusion
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 10: Course projects examples – Application using IoT platforms, sensors, actuators etc
Something interesting that uses sensor, IoT platforms, actuators
  Has a research question to be tackled;
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 11: Let’s look at some commonly used IoT devices
Notes: Backscatter communication actually help us overcome this limitation

## Slide 12: What’s inside Apple AirTag
Nordic Semiconductor nRF52832 Bluetooth low-energy SoC w/NFC controller
Notes: Backscatter communication actually help us overcome this limitation

## Slide 13: What’s inside Apple AirTag
Accelerometer: Bosch Sensortec BMA28x 3-axis accelerometer
SoC/Microcontroller: Nordic Semiconductor nRF52832 Bluetooth low-energy SoC w/NFC controller
Actuator: Speaker
And many other componets….
Notes: Backscatter communication actually help us overcome this limitation

## Slide 14: Let’s look at some commonly used IoT devices
Notes: Backscatter communication actually help us overcome this limitation

## Slide 15: Let’s look at some commonly used IoT devices
MediaTek MT3333 GPS SoC
Bosch Sensortec BHI160 Accelerometer/Gyroscope w/ Sensor Hub
STMicroelectronics LIS2DW12 MEMS 3-Axis Accelerometer
Fitbit FBT18SW ARM application processor
Notes: Backscatter communication actually help us overcome this limitation

## Slide 16: Let’s look at some commonly used IoT devices
Notes: Backscatter communication actually help us overcome this limitation

## Slide 17: Let’s look at some commonly used IoT devices
Actuator, very important: 85 dB horn for alarm
Freescale SCK60DN512VLL10 custom Kinetis K60 low-power 100 MHz MCU (Cortex based)
Silicon Labs EM357 Ember Zigbee SoC
Murata Type ZX 2.4 GHz Wi-Fi 802.11b/g/n module (with Broadcom BCM43362 chipset)
Notes: Backscatter communication actually help us overcome this limitation

## Slide 18: TraceTogether Token
Notes: Backscatter communication actually help us overcome this limitation

## Slide 19: Four components of internet of things device
Computation and Storage
Sensing and Actuation
Power
Wireless Connectivity
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 20: What is at the heart of computers and IoT?
Microprocessor
  Usually, they don’t have peripherals or memory
  CPU+Pins (No memory, peripherals)
  Your computer has a microprocessor
Microcontrollers
  We deal with them mostly in embedded and IoT devices
  Memory + Peripherals + CPU + Pins
  Peripherals: Specialized hardware units within the chip
Notes: Backscatter communication actually help us overcome this limitation

## Slide 21: What is at the heart of computers and IoT?
System on chips (SoC)
  Microcontroller + Extensive Peripherals
  Example: Radios or ML Accelerators
  Essentially multiple chips combined
Dedicated accelerator chips
  Designed for a very specific purpose like for speech detection
Notes: Backscatter communication actually help us overcome this limitation

## Slide 22: Microcontroller outside IoT

## Slide 23: What is a microcontroller?
A microcontroller (MCU) is a small computer on a single integrated circuit consisting of a relatively simple central processing unit (CPU) combined with peripheral devices such as memories, I/O devices.

## Slide 24: Microcontroller VS Microprocessor

## Slide 25: Block diagram of a microcontroller
Microcontroller
Processor
Memory
Peripherals
Pins
Notes: Backscatter communication actually help us overcome this limitation

## Slide 26: Die shot of a microcontroller

## Slide 27: Older microcontrollers (90s-00s)
Cheap , small computer systems
PIC
  8, 16, and 24-bit MIPs architecture
  PICAXE available with Basic interpreter
AVR
  8-bit custom architecture (AVR architecture)
  Used in Arduinos
  AT Tiny 4: $0.30 per unit
    4 I/O pins, 32 Bytes RAM, 512 Bytes ROM

## Slide 28: More capable microcontrollers (00s-10s)
Diversify into extreme low power and more capable systems
MSP430
  16-bit custom architecture (MSP430 architecture)
  Capable, but also extremely low power
    <1 μA sleep current
STM32, Atmel SAM series (Cortex-M0, M3, M4, M4F)
  32-bit ARM architecture (ARMv7)
    Leverage success of ARM on smartphones
  Every peripheral under the sun. Plus a variety of memory choices

## Slide 29: Cortex M Series
A number of options for increasing capabilities
In practice:
  Cortex-M0+ for low-end systems
  Coretx-M4 for high capability systems

## Slide 30
Fourth quarter of 2020. Arm shipped 4.4 billion Cortex-M processors
ARM Press Release (Feb 11, 2021) reporting on Fourth Quarter 2020
Trillion embedded devices will be deployed soon
Notes: ++ Due to the numerous applications that the internet of things enables, we are witnessing a massive growth in the number of microcontrollers being sold. These microcontrollers form the heart of the IoT platforms.
++ To illustrate this point: ARM, a popular UK based company, just reported numbers, and in these numbers, they state that they sold 4.4 billion cortex M processors in just one quarter. These microcontrollers are almost exclusively used on IoT platforms, which demonstrates the massive growth we are witnessing in the number of deployed IoT devices.
++ If this growth continues, and in fact, I believe this growth will accelerate, we will soon have a trillion embedded devices that are going to be deployed in the world.

## Slide 31: Modern system-on-chips (10s-?)
Focus: increase memory and capability
  Include radios in the same chip
  Machine learning accelerators and other dedicated functionality
nRF51 and nRF52 series
  32-bit ARM microcontrollers (Cortex M)
  Include 2.4 GHz radio: Bluetooth Low Energy and 802.15.4/Thread
Others have followed this same path
  TI CC26XX
  Apollo3
  STM32WL

## Slide 32: Future microcontrollers
Multi-core systems
  Not for performance, but for separation of concerns
    Run radio code on one core
    Application code goes on the other core
  Also allows BIG.little architecture
    Higher performance core when interpreting data
    Lower performance core for sampling sensors
  nRF53 series is already doing this
    But support is still nascent

## Slide 33: Types of Microcontrollers

## Slide 34: Processor design choices for embedded
How many bits is the architecture?
  8-bit and 16-bit not uncommon
  64-bit is very rare (who has that much memory?)
What instructions are supported?
  Normal stuff yes
  What about single-cycle multiply?
  What about floating-point operations?
  Vector instructions?
How fast does it run?
  1-100 MHz is common on modern systems (faster is more energy cost)
  Occasionally MUCH slower (think 32 KHz)

## Slide 35: Peripherals on microcontrollers
Hardware modules that perform some action
Common examples
  Control digital input and output pins
  Read analog inputs
  Send messages in a given wire protocol (UART, SPI, I2C)
  Set and check timers
Less common examples
  Cryptography accelerators
  Complicated wire protocols (USB, CAN)
  Wireless radios (BLE, 802.15.4, WiFi)

## Slide 36: Peripheral design choices
More peripherals mean more use cases
  But also means more cost for the chip
  Peripherals occupy silicon
  Most peripherals will go unused for a given application…
Flexibility within a given peripheral
  One capability is easier to use
  Many capabilities are more useful
Apple A8 SoC

## Slide 37: Connecting peripherals on microcontrollers
Peripherals need to electrically connect to outside world
  Attach to pins on the exterior of the chip
More pins allow for more connections
  At increased cost and size
Pin layouts can add more pins for cheaper
  But make soldering and debugging difficult
Peripherals need to connect to external pins
  Modern microcontrollers allow any-to-any connections

## Slide 38: Memory on microcontroller (hierarchy)
Registers
RAM
ROM

## Slide 39: Volatile memory: SRAM
Same design as registers in traditional computer systems
  No need to refresh it -> lower energy costs
Tradeoff:
  More expensive
  Physically larger

## Slide 40: Non-Volatile memory: Flash (usually)
Same design as SSDs and Flash drives
Memory is stored with no energy costs
  Reading is lowish energy and quick
  Writing is high energy and very slow
    Writing also has to occur in blocks (e.g. 512 bytes)
Concern: Flash has a limited lifetime ~10,000 writes
  Only writing to Flash when you load code? Essentially forever
  Recording data to Flash every second? 2.8 hours

## Slide 41: SRAM (RAM) versus Flash (ROM) memory
Size and time difference between non-volatile and volatile memory is significantly reduced from traditional computing
  Non-volatile store 2-10x larger than volatile
  Single-cycle RAM. Maybe two-cycles to Flash (to read)
Major difference: energy and writability
  SRAM is low-energy to read and write (no refresh needed)
  Flash is lowish-energy to read, but very high energy to write
Hierarchical structure is not enforced
  Same address space for RAM and Flash (very different from traditional)
  Run instructions right inside of Flash
  Keep variables in RAM (or const variables in Flash)

## Slide 42: FRAM and MRAM
FRAM and MRAM are both rising protentional Flash replacements
  Non-volatile
  Writable at the byte level
  Very high to infinite write/erase cycles
  Lower energy costs for writing and reading
The two-use unrelated magnetic techniques for data storage
Starting to appear in microcontrollers
  TI MSP430s have used 16 kB FRAM
  Apollo4 (ARM Cortex-M4F) has 2 MB of MRAM

## Slide 43: How to choose microcontrollers for projects ?
What metrics we need to consider?
  Power consumption
  Clock frequency
  IO pins
  Memory
  Internal functions
  Others

## Slide 44: Microcontrollers with neural networks
Very low-power for specific tasks. Voice detection at hundreds of microwatts of power consumption

## Slide 45: Microcontrollers with neural networks
Very low-power for specific tasks. Voice detection at hundreds of microwatts of power consumption

## Slide 46: Case study: LoRea and Edison Tag

## Slide 47: Case study: LoRea backscatter tag
Microcontroller: MSP430FR5969, 100 uA/MHz
Clock rate: 16 MHz CPU
Memory: 64 kB FRAM, 2 kB SRAM
Peripherals: ADC,DMA, UART, Timer
Pins: 38 to 48 depending on the package type

## Slide 48: Energy harvesting can lead to intermittent computing

## Slide 49: Disabling the microcontroller
Even 2 μA sleep current might be too much for energy harvesting
  Can turn off microcontroller periodically
  Enable it again once VCC returns
Problem: how do you write software to deal with intermittency?
  Run-to-completion with relatively quick code
    Initialize, sample sensor, send packet, turn off again
  Code checkpointing
    Save state from code and restore when power resumes
    Might be as little as which state the system is in, plus some samples
    Might be as much as saving entire stack state
    Needs low-energy, nonvolatile storage (FRAM or MRAM help!)

## Slide 50
Programs may not finish
Execution Time
count++
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.
Make capy bigger

## Slide 51
Programs may not finish
Execution Time
count++
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
count++;
buf[count] = accel()
.
.
.
Power fail
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 52
Programs may not finish
Execution Time
count++
buf[count] = accel()
count++;
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Power fail
.
.
.
Need to latch execution state periodically!
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 53
Checkpointing enables progress
Execution Time
count++
buf[count] = accel()
count++;
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Power fail
.
.
.
Need to latch execution state periodically!
count++
buf[count] = accel()
Power fail
Checkpoint
Execute with checkpoints
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 54
Checkpointing enables progress
Execution Time
count++
buf[count] = accel()
count++;
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Power fail
.
.
.
Need to latch execution state periodically!
count++
buf[count] = accel()
buf[count] = accel()
avg = sum(buf)/count
transmit-
Power fail
Power fail
Checkpoint
Checkpoint
Execute with checkpoints
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 55
Checkpointing enables progress
Execution Time
count++
buf[count] = accel()
count++;
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Power fail
.
.
.
Need to latch execution state periodically!
count++
buf[count] = accel()
buf[count] = accel()
avg = sum(buf)/count
transmit-
Power fail
Power fail
Checkpoint
Checkpoint
transmit(avg)
Execute with checkpoints
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 56: Instructional video (Raspberry PI)

## Slide 57: Platforms to prototype IoT Applications: Microbit

## Slide 58: Platforms to prototype IoT Applications: Arduino Nano 33 BLE

## Slide 59: Platforms to prototype IoT Applications: Raspberry Pi 4

## Slide 60: Platforms to prototype IoT Applications: Other platforms

## Slide 61: nRF52833 – Microcontroller on the Micro:bit v2
32-bit ARM Cortex-M4F microcontroller
  64 MHz core, 128 KB RAM, 512 KB Flash
  Floating point support
  2.4 GHz Radio: Bluetooth Low energy / 802.15.4
  Various peripherals
    ADC, PWM
    I2C, UART, SPI, USB
    RNG, 32-bit Timers, Watchdog, Temperature
    Up to 42 I/O pins

## Slide 62: Last mandatory reading of the course 
System Architecture Directions for Post-SoC/32-bit Networked Sensors – ACM SenSys 2018
Due end of next-to-next week, 16th of October 2022
Notes: Backscatter communication actually help us overcome this limitation

## Slide 63: CS 6204 – Special Topics in Internet of Things
Ambuj Varshney
ambujv@nus.edu.sg
http://ambuj.se
Notes: Good morning/afternoon everyone. Thank you for inviting me for giving this talk.
In this talk, I will describe my effort to design ubiquitous Internet of Things systems.
In the end of the talk: I will cover some of the future research directions that I would like to address as a faculty member.